## General settings
Baudrate: 125kbps
Message identifier: standard 11bit
## Message identifier
Bits:
10	9	8	7	6	5	4	3	2	1	0
A	Command					Address

A	the ack bit. For commands that need to be ack'ed, this can be used for the returning	package. The ack package should have dlc set to 0.
Address	the node address from 0 to 32. 0 to 3 should be reserved for masters (pc).
Address can be source or destination.
Command	explained in the “Commands” section. It ranges from 0 to 32.

## Commands
Short table
ID	Name	Length	Cyclic	Master/Slave / sends	Needs Ack	Comment
0	MSG_STATUS_UPTIME	6	1s	Slave	No
1	MSG_STATUS_RELAIS	1	250ms	Slave	No
2	MSG_STATUS_HR20_TEMPS	5	1s	Slave	No	Only if HR20 enabled
3	MSG_STATUS_HR20_MISC	5	1s	Slave	No	Only if HR20 enabled
4	MSG_STATUS_CONFIG	2	No	Slave	No	On request
7	MSG_CMD_BOOTLOADER	0	No	Master	No	Bootloader vector jump
8	MSG_CMD_RESET	0	No	Master	No	Reset vector jump
9	MSG_CMD_RELAIS	2	No	Both	Yes	Set relais
10	MSG_CMD_CONFIG_SET	2	No	Master	Yes	Set config (eeprom)
11	MSG_CMD_CONFIG_GET	1	No	Master	No	Get config
12	MSG_HR20_SET_T	1	No	Master	Yes
13	MSG_HR20_SET_MODE_MANU	0	No	Master	Yes
14	MSG_HR20_SET_MODE_AUTO	0	No	Master	Yes
15	MSG_HR20_SET_TIME_DATE	6	No	Master	Yes

### MSG_STATUS_UPTIME
Identifier	0
Data Length Code	6
Cyclic	every second
Slave
Data bytes:
0	1	2	3	4	5
Version	Uptime[31..24]	Uptime[23..16]	Uptime[15..8]	Uptime[7..0]	Voltage

Version	uint8_t anything allowed
Uptime	uint32_t in seconds
Voltage	uint8_t measured voltage in volts * 10 (50 = 5V)

### MSG_STATUS_RELAIS
Identifier	1
Data Length Code	1
Cyclic	every 250ms
Slave
0
Relais

Relais	uint8_t status of the four relais (bits 3..0)

Other nodes can parse this packet to show the status of a relais on its LEDs.

### MSG_STATUS_HR20_TEMPS TBD
Identifier	2
Data Length Code	1
Cyclic	Yes, every 250ms
Slave
0
Relais

Relais	uint8_t status of the four relais (bits 3..0)

### MSG_STATUS_HR20_MISC TBD
Identifier	2
Data Length Code	1
Cyclic	Yes, every 250ms
Slave
0
Relais

Relais	uint8_t status of the four relais (bits 3..0)

### MSG_STATUS_CONFIG
Identifier	4
Data Length Code	2
Cyclic	No
Slave
0	1
Type	Value

Type	See section “Configurable stuff”
Value	Value of type
### MSG_CMD_CONFIG_SET
Identifier	10
Data Length Code	2
Cyclic	No
Master
0	1
Type	Value

Type	See section “Configurable stuff”
Value	Value of type

Sets some configurables like the node address or mode. More usally one will want to set the destination node addresses and relais for the six buttons.

### MSG_CMD_CONFIG_GET
Identifier	11
Data Length Code	1
Cyclic	No
Master
0
Type

Type	See section “Configurable stuff”

Get a configurable. This will force the node to send back MSG_STATUS_CONFIG

## Configurable stuff

ID	Name	Description
0	CONF_NODE_ADDRESS	Address of the node
1	CONF_MODE	Mode of the node (see section “Modes”)
2	CONF_BANDGAP	Calibrate bandgap voltage
3	CONF_BUTTON_1_ADDRESS	Destination address for button 1
4	CONF_BUTTON_1_RELAIS	Destination relais at address for button 1
5	CONF_BUTTON_2_ADDRESS
6	CONF_BUTTON_2_RELAIS
7	CONF_BUTTON_3_ADDRESS
8	CONF_BUTTON_3_RELAIS
9	CONF_BUTTON_4_ADDRESS
10	CONF_BUTTON_4_RELAIS
11	CONF_BUTTON_5_ADDRESS
12	CONF_BUTTON_5_RELAIS
13	CONF_BUTTON_6_ADDRESS
14	CONF_BUTTON_6_RELAIS

## Modes
ID	Name	Description
1	MODE_HR20	Node has connection to hr20 (excludes uart master)
2	MODE_UART_MASTER	Node has USB PC connection (excludes hr20)
4	MODE_HEINZUNGS_MASTER	Node is HEINZUNG_MASTER
8	MODE_BLUBB_COUNTER	Node is BLUBB_COUNTER